## Slide 1: FLOATING POINT NUMBER REPRESENTATION
20XC14 DIGITAL SYSTEM DESIGN

## Slide 2
Need for floating point number
Binary representation of floating point Numbers
Computer representation of floating point numbers
IEEE 754

## Slide 3: Why do we need floating point?
Many numeric applications need numbers over a huge range
  e.g., nanoseconds to centuries
  Most scientific applications require real numbers (e.g. )
But so far we only have integers. What do we do?
  We could implement the fractions explicitly
    e.g.: ½, 1023/102934
  We could use bigger integers
    e.g.: 64-bit integers
  Floating-point representation is often better
    has some drawbacks too!

## Slide 4: Floating Decimal Point : Scientific Form

## Slide 5: Floating Point Notation
Decimal
  12.456810 (decimal notation) means
      10*1 + 2 + 4/10 + 5/100 + 6/1000 + 8/10000
  In scientific notation
    12.4568 =
      124568 * 10-4 = 1245680 * 10-5 =
      12456.8 * 10-3 = 1245.68 * 10-2 =
      124.568 * 10-1 =12.4568 * 100
      1.24568 * 101
    1.24568*101 is an example of normalised scientific notation.

## Slide 7: Floating Point in Binary
Binary
  0.010011two =
    (0/2) + (1/22) + (0/24) +(1/25) + (1/26)
      0 + 1/4 + 0 + 1/32 + 1/64 =
      (0.25 + 0.03125 + 0.015625)10 =
      0.296875 10
In scientific notation
  10011*2-6 = 1001.1*2-5 =
  100.11*2-4
  1.0011*2-2 normalised

## Slide 8: COMPUTER REPRESENTATION OF FLOATING POINT NUMBERS
In the CPU, a 32-bit floating point number is represented using IEEE standard format as follows:
S | EXPONENT | MANTISSA
where S is single bit, the EXPONENT is 8 bits, and the MANTISSA is 23 bits
The mantissa represents the leading significant bits in the number.
The mantissa is said to be normalized when it is expressed as a value between 1 and 2. i.e., the mantissa would be in the form 1.xxxx
The leading integer of the binary representation is not stored. Since it is always a 1, it can be easily restored

## Slide 9
The "S" bit is a sign bit and indicates whether the value represented is positive or negative(0 for positive, 1 for negative)
The exponent is used to adjust the position of the binary point
If a number is smaller than 1, normalizing the mantissa will produce a negative exponent. (Ex: 0.010011 = 1.0011*2-2 normalized)
2 sign bits ??( Mantissa and Exponent)
But 127 is added to all exponents in the floating point representation, allowing all exponents to be represented by a positive number (BIASED EXPONENT)

## Slide 10
IEEE 754 FLOATING POINT
REPRESENTATION

## Slide 11: FLOATING POINT STANDARD
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)

## Slide 12: Biased Representation - (IEEE FP Standard)
The ‘bias’ 127 represents 0
128 to 255 represent positive exponents
1 to 127 represent negative exponents
  (remember 0 is reserved for the entire number being zero).
The actual exponent is therefore:
  E - bias
(-1)S * (1 + significand) * 2E-bias

## Slide 13
IEEE representation
Actual Value

## Slide 14
IEEE representation
Actual Value

## Slide 15: FLOATING-POINT EXAMPLE

## Slide 16: FLOATING-POINT EXAMPLE

## Slide 17: Binary Floating-Point Notation
Example: (0x42280000 in hexadecimal)
Three fields:
  Sign bit (S)
  Exponent (E): Unsigned “Bias 127” 8-bit integer
    E = Exponent + 127
    Exponent = 10000100 (132) – 127 = 5
  Significand (F): Unsigned fixed binary point with “hidden-one”
    Significand = “1”+ 0.01010000000000000000000 = 1.3125
  Final value: N = -1S (1+F) x 2E-127 = -10(1.3125) x 25 = 42
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0
“F” Significand (Mantissa) - 1
“E”
Exponent + 127
“S”
Sign Bit
1 | 0 | 0 | 0 | 0 | 1 | 0 | 0

## Slide 18: Binary Codes - Increasing Precision
Representation of Floating Point Numbers- Example of the IEEE 754 standard
    Single precision 32 bit floating point format
    For this example:
      Sign = 0, hence, a positive number
      Exponent = 124, hence,
      Fraction = 1.0100…02= 1+0x2-1+1x2-2+0x2-3+… = 1.2510
    Hence, the number is +1.25/8 = 0.1562510
= 0.1562510

## Slide 19: Example
19
1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Sign
(s)
Biased
Exponent (E)
Mantissa (m)

## Slide 20
Example 1. Represent the decimal value 2.5 in 32-bit floating point format.
2.5 = 10.1b
In normalized form, this is: 1.01 * 21
The mantissa: M = 01000000000000000000000 …..(23 bits without the leading 1)
The exponent: E = 1 + 127 = 128 = 10000000b
The sign: S = 0 (the value stored is positive)
So, 2.5 = 0 10000000 01000000000000000000000

## Slide 21
Example 2: Represent the number -0.00010011b in floating point form.
0.00010011b = 1.0011 * 2-4
Mantissa: M = 00110000000000000000000 (23 bits with the integral 1 not represented)
Exponent: E = -4 + 127 = 01111011b
S = 1 (as the number is negative)
Result: 1 01111011 00110000000000000000000

## Slide 22
One
Sign = +, Exponent = 0, Significand = 1.0
1 = -10 (1.0) x 20
S = 0, E = 0 + 127, F = 1.0 – ‘1’
0 01111111 00000000000000000000000 = 0x3f800000
One-half
Sign = +, Exponent = -1, Significand = 1.0
½ = -10 (1.0) x 2-1
S = 0, E = -1 + 127, F = 1.0 – ‘1’
0 01111110 00000000000000000000000 = 0x3f000000
Minus Two
Sign = -, Exponent = 1, Significand = 1.0
-2 = -11 (1.0) x 21
1 10000000 00000000000000000000000 = 0xc0000000

## Slide 23: SINGLE PRECISION RANGE

## Slide 24: DOUBLE-PRECISION RANGE

## Slide 25: Zeros
How do you represent 0?
  Sign = ?, Exponent = ?, Significand = ?
    Here’s where the hidden “1” comes back to bite you
    Hint: Zero is small. What’s the smallest number you can generate?
      Exponent = -127, Signficand = 1.0
      -10 (1.0) x 2-127 = 5.87747 x 10-39
IEEE Convention
  When E = 0 (Exponent = -127), we’ll interpret numbers differently…
    0 00000000 00000000000000000000000 = 0 not 1.0 x 2-127
    1 00000000 00000000000000000000000 = -0 not -1.0 x 2-127

## Slide 26: Infinities
IEEE floating point also reserves the largest possible exponent to represent “unrepresentable” large numbers
  Positive Infinity: S = 0, E = 255, F = 0
    0 11111111 00000000000000000000000 = +∞
    0x7f800000
  Negative Infinity: S = 1, E = 255, F = 0
    1 11111111 00000000000000000000000 = -∞
    0xff800000
  Other numbers with E = 255 (F ≠ 0) are used to represent exceptions or Not-A-Number (NAN)
    √-1, -∞ x 42, 0/0, ∞/∞, log(-5)
  It does, however, attempt to handle a few special cases:
    1/0 = + ∞, -1/0 = - ∞, log(0) = - ∞

## Slide 27: Special Exponents and Numbers
all zeros
all ones
s |  | m | Represents
0 | all zeros | all zeros | 0
1 | all zeros | all zeros | -0
0 | all ones | all zeros | 
1 | all ones | all zeros | 
0 or 1 | all ones | non-zero | NaN

## Slide 28: Summary of Floating Point Real Number Encodings
NaN
NaN
+

0
+Denorm
+Normalized
-Denorm
-Normalized
+0