## Slide 1: BOOLEAN ALGEBRA and LOGIC GATES
20XC14 DIGITAL SYSTEM DESIGN

## Slide 2: Lecture Outline
Introduction
Basic Operations: NOT, AND, OR
Representations of Boolean Expressions
Basic Boolean Theorems
Implementation of Boolean Expressions

## Slide 3: Overview
Gate Circuits and Boolean Equations
  Binary Logic and Gates
  Boolean Algebra
  Standard Forms
Circuit Optimization
  Two-Level Optimization
  Map Manipulation
  Multi-Level Circuit Optimization
Additional Gates and Circuits
  Other Gate Types
  Exclusive-OR Operator and Gates
  High-Impedance Outputs

## Slide 4: Binary Logic and Gates
Binary variables take on one of two values.
Logical operators operate on binary values and binary variables.
Basic logical operators are the logic functions AND, OR and NOT.
Logic gates implement logic functions.
Boolean Algebra: a useful mathematical system for specifying and transforming logic functions.
We study Boolean algebra as foundation for designing and analyzing digital systems!

## Slide 5: Binary Variables
Recall that the two binary values have different names:
  True/False
  On/Off
  Yes/No
  1/0
We use 1 and 0 to denote the two values (True/False)
Variable identifier examples:
  A, B, y, z, or X1 for now
  RESET, START_IT, or ADD1 later

## Slide 6: Boolean Algebra- Introduction
Boolean Algebra
  In 1849 George Boole published a scheme for the algebraic description of logic processes
  In the 1930’s Claude Shannon used Boolean Algebra to describe circuits built with switches
Boolean Algebra is an effective tool for describing logic circuits

## Slide 7: Boolean Algebra -Boolean Logic
Two logic levels
  TRUE = HIGH = 1
  FALSE = LOW = 0
+5
V
0
1
0
1
T
ime
Transition from logic 1 to logic 0
does not take place instantaneously
in real digital systems
+5
V
0
Logic 1
Logic 0
Intermediate values may be visible
for an instant
Time

## Slide 8: Boolean Algebra -Basic Operations: NOT, AND, OR
Logical NOT
  Description:
    The output is the complement/inverse/opposite of the input
  Symbolic Representation (NOT gate):
  Truth Table Representation:
  Boolean Description: C = NOT A
A
C
A | C
0 | 1
1 | 0
A | C
F | T
T | F
or C = A’
or C =

## Slide 9: Boolean Algebra-Basic Operations: NOT, AND, OR
Logical AND
  Description:
    The output is TRUE if and only if all the inputs are TRUE
  Symbolic Representation (AND gate):
  Truth Table Representation:
  Boolean Description: C = A AND B
A | B | C
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | C
F | F | F
F | T | F
T | F | F
T | T | T
or C = AB
or C = A B

## Slide 10: Boolean Algebra- Basic Operations: NOT, AND, OR
Logical OR
  Description:
    The output is TRUE if any of the inputs are TRUE
  Symbolic Representation (OR gate):
  Truth Table Representation:
  Boolean Description: C = A OR B
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | B | C
F | F | F
F | T | T
T | F | T
T | T | T
  or C = A + B

## Slide 11: Boolean Algebra Logic Gates and Boolean Expressions
Derive an expression for the output of this logic circuit?
  Eventually we will omit the “” in the AND gate and “+” in the OR gate
The logic expression is a function of three variables (A, B, and C).
B’
AB’
AB’+C

## Slide 12: Boolean Algebra -logic Gates and Boolean Expressions
Derive an expression for the output of this logic circuit?
The output is which may also be written as [A(C+D)]’+BE
  This expression has five variables (A, B, C, D, and E)
C+D
A(C+D)
BE
+

## Slide 13: Boolean Algebra-Logic Gates and Boolean Expressions
Literals
  Each appearance of a variable or its complement in an expression is referred to as a literal.
  Example:
  The expression has three variables (A, B, and C)
  The expression has 10 literals
AB’C+A’B+A’BC’+B’C’

## Slide 14: Boolean Algebra- Truth Tables of a Logic Circuit
Determine the truth table for the output (F) of the logic circuit
A | B
0 | 0
0 | 1
1 | 0
1 | 1
A’
1
1
0
0
F=A’+B
1
1
0
1
Two variables
Four possible inputs (i.e. 2n)

## Slide 15: Boolean Algebra - Truth Tables of a Logic Circuit
A+C
0
1
0
1
1
1
1
1
B’+C
1
1
0
1
1
1
0
1
A+C
B’+C
(A+C)(B’+C)
0
1
0
1
1
1
0
1
(A+C)(B’+C)
B’
1
1
0
0
1
1
0
0
A
0
0
0
0
1
1
1
1
B
0
0
1
1
0
0
1
1
C
0
1
0
1
0
1
0
1

## Slide 16: Logic Function Implementation
Using Switches
  For inputs:
    logic 1 is switch closed
    logic 0 is switch open
  For outputs:
    logic 1 is light on
    logic 0 is light off.
  NOT uses a switch such that:
    logic 1 is switch open
    logic 0 is switch closed
Switches in series => AND
Switches in parallel => OR
C
Normally-closed switch => NOT

## Slide 17: Logic Function Implementation (Continued)
Example: Logic Using Switches
Light is on (L = 1) for
  L(A, B, C, D) =
  and off (L = 0), otherwise.
Useful model for relay circuits and for CMOS gate circuits, the foundation of current digital logic technology
B
A
D
C
Notes: L (A, B, C, D) = A ((B C') + D) = A B C' + A D

## Slide 18: Logic Gates
In the earliest computers, switches were opened and closed by magnetic fields produced by energizing coils in relays. The switches in turn opened and closed the current paths.
Later, vacuum tubes that open and close current paths electronically replaced relays.
Today, transistors are used as electronic switches that open and close current paths.

## Slide 19: Logic Gate Symbols and Behavior
Logic gates have special symbols:
= =
And waveform behavior in time as follows:
=

## Slide 20: BOOLEAN ALGEBRA - terminologies
The complement of a variable, A, is its inverse,
The variable or its complement is called a literal.
A is the true form of the variable and the A’ is the complementary form
The AND of one or more literals is called a product or an implicant.
A minterm is a product involving all of the inputs to the function.
ABC’ is a minterm for a function of the three variables A, B, and C
maxterm is a sum involving all of the inputs to the function(A+B’+C)

## Slide 21: Boolean Algebra - Basic Boolean Theorems
Basic Theorems
  Principle of DUALITY:
    Given any Boolean expression its DUAL expression can be obtained by:
      Replace “ • “ by “ + “ (and vice versa), also
      Replace “ 0 “ by “ 1 “ (and vice versa)

## Slide 22: Boolean Algebra
Axioms and theorems of Boolean algebra obey the principle of duality.

## Slide 23: Boolean Algebra - Basic Boolean Theorems
Basic Theorems
  Operations with 0 and 1
x0 = 0
x1 = x
x | 0 | x0
0 | 0 | 0
1 | 0 | 0
x | 1 | x1
0 | 1 | 0
1 | 1 | 1
x+0 = x
x+1 = 1
x | 0 | x+0
0 | 0 | 0
1 | 0 | 1
x | 1 | x+1
0 | 1 | 1
1 | 1 | 1
Expression
Dual of Expression

## Slide 24: Boolean Algebra -Basic Boolean Theorems
Idempotent Law:
Laws of Complementarity
Involution Law
x + x = x
x  x = x
Expression
Dual of Expression
= 0
Expression
Dual of Expression
= 1

## Slide 25: Boolean Algebra -More Boolean Theorems
Commutative Law
Associative Law
Distributive Law
x  y = y  x
Expression
Dual of Expression
x + y = y + x
(x  y)  z = x  (y  z)
Expression
Dual of Expression
(x + y) + z = x + (y + z)
x  (y + z) = (x  y) + (x  z)
Expression
Dual of Expression
x + (y  z) = (x + y)  (x + z)

## Slide 27: how to prove that a theorem is true
Perfect induction
In Boolean algebra, proofs of theorems with a finite number of variables are easy
Show that the theorem holds for all possible values of these variables.
  In Boolean equations, NOT has the highest precedence, followed by AND, then OR
  Can be done with a truth table also.

## Slide 28: Boolean Algebra -Boolean Algebra Examples
Distributive Law
LHS
Complementary Law
  Operations with 0 and 1
LHS
  Operations with 0 and 1
Distributive Law
  Operations with 0 and 1
Prove the following algebraically

## Slide 29: Boolean Algebra - Boolean Algebra Examples
LHS
  Last example: X+XZ = X
Distributive Law (Dual)
  Idempotent Law
Distributive Law
  Last example: X+XY = X
OR
Examples:

## Slide 30: Boolean Algebra -A Circuit Example
x + (y  z) = (x + y)  (x + z)
Distributive Law (Dual)
Determine the Output of the Following Circuit
Design a Simpler Circuit with the Same Output

## Slide 31: Boolean Algebra More Boolean Theorems
y + z
0
1
1
1
0
1
1
1
x (y + z) = x y + x z
x(y + z)
0
0
0
0
0
1
1
1
LHS
x y
0
0
0
0
0
0
1
1
x z
0
0
0
0
0
1
0
1
RHS
x y + x z
0
0
0
0
0
1
1
1
y + z
x(y + z)
x y
x z
x y + x z
x | y | z
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
x | y | z
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
Let’s verify the Distributive Law via a truth table

## Slide 32
Review of Commutative, Associative, and Distributive Laws
DeMorgan’s Law
Simplification Theorems

## Slide 33: Boolean Algebra Review of Commutative Law
Commutative Law
x  y = y  x
Expression
Dual of Expression
x + y = y + x
x
y
y
x


x
y
y
x

## Slide 34: Boolean Algebra -Review of Associative Law
Expression
Dual of Expression
z
y
x
(x  y)  z = x  (y  z)
(x + y) + z = x + (y + z)

x
z
y
y
x
z

z
y
x

y
x
z
x  y  z

y
x
z
x + y + z
LHS
RHS
LHS
RHS
Associative Law

## Slide 35: Boolean Algebra -Review of Distributive Law
x  (y + z) = x  y + x  z
Expression
Dual of Expression
x + y  z = (x + y)  (x + z)
z
y
x
y
x

z
x
x
z
y
y
x
z
x
LHS
RHS
LHS
RHS
Distributive Law

## Slide 36: Boolean Algebra -DeMorgan’s Law
Expression
Dual of Expression
=
=
x | y
0 | 0
0 | 1
1 | 0
1 | 1
x+y
0
1
1
1
1
0
0
0
1
0
0
0
1 | 1
1 | 0
0 | 1
0 | 0
1 | 1
1 | 0
0 | 1
0 | 0
1
0
0
0
1
0
0
0
LHS
RHS
x | y
0 | 0
0 | 1
1 | 0
1 | 1
0
0
0
1
0
0
0
1
1
1
1
0
1
1
1
0
1 | 1
1 | 0
0 | 1
0 | 0
1 | 1
1 | 0
0 | 1
0 | 0
1
1
1
0
1
1
1
0
LHS
RHS

## Slide 37: Boolean Algebra -DeMorgan’s Law
DeMorgan’s Law
DeMorgan’s Law via gates
Expression
Dual of Expression
=
=
y
x

y
x
y
x

y
x
LHS
RHS
LHS
RHS


## Slide 38: Boolean Algebra DeMorgan’s Law
LHS
RHS
RHS
LHS
DeMorgan’s Law via “pushing bubbles”
Expression
Dual of Expression
=
=
y
x

y
x
LHS
RHS
y
x

y
x
LHS
RHS
DeMorgan’s Law

## Slide 39: Boolean Algebra Simplification Theorems

## Slide 40: Boolean Algebra - Examples
Simplify the following circuit
Simplify:

A
B

## Slide 42: Next Lecture
Sum of Products / Product of Sums
Exclusive OR operation
Simplification
Proving equations (Validity)