## Slide 1: SOP and POS forms
20XC14 DIGITAL SYSTEM DESIGN

## Slide 2: Lecture Outline
Sum of Products / Product of Sums
Multiplying out and Factoring
Exclusive OR operation
Simplification
Proving equations (Validity)

## Slide 3: Standard Forms of Boolean Expressions
All Boolean expressions, regardless of their form, can be converted into either of two standard forms:
The sum-of-products (SOP) form
The product-of-sums (POS) form
Standardization makes the evaluation, simplification, and implementation of Boolean expressions much more systematic and easier.

## Slide 4: Sum OF Products(SOP)

## Slide 5: Sum of Products (SOP)
PRODUCTs
A sum of only products
An AND – OR circuit!!!
SUMs
How can we implement SOP expressions?

## Slide 6: The Sum-of-Products (SOP) Form

## Slide 8: STANDARD SOP FORM

## Slide 10: Converting Product Terms to Standard SOP
Step 1: Multiply each nonstandard product term by a term made up of the sum of a missing variable and its complement. This results in two product terms.
As you know, you can multiply anything by 1 without changing its value.
Step 2: Repeat step 1 until all resulting product term contains all variables in the domain in either complemented or uncomplemented form. In converting a product term to standard form, the number of product terms is doubled for each missing variable.

## Slide 11: Converting Product Terms to Standard SOP (example)

## Slide 12: Product of Sums (POS)

## Slide 13: Product of Sums (POS)
PRODUCTs
SUMs
A product of only sums
An OR – AND circuit!!!
How can we implement POS expressions?

## Slide 14: PRODUCT OF SUM EXPRESSION

## Slide 15: Standard POS form

## Slide 16: Converting a Sum Term to Standard POS
Step 1: Add to each nonstandard product term a term made up of the product of the missing variable and its complement. This results in two sum terms.
As you know, you can add 0 to anything without changing its value.
Step 2: Apply rule A+BC=(A+B)(A+C).
Step 3: Repeat step 1 until all resulting sum terms contain all variable in the domain in either complemented or uncomplemented form.

## Slide 17: Converting a Sum Term to Standard POS (example)

## Slide 18: SOP/POS

## Slide 19: Converting Standard SOP to Standard POS
The Facts:
The binary values of the product terms in a given standard SOP expression are not present in the equivalent standard POS expression.
The binary values that are not represented in the SOP expression are present in the equivalent POS expression.

## Slide 20: Converting Standard SOP to Standard POS
What can you use the facts?
Convert from standard SOP to standard POS.
How?
Step 1: Evaluate each product term in the SOP expression. That is, determine the binary numbers that represent the product terms.
Step 2: Determine all of the binary numbers not included in the evaluation in Step 1.
Step 3: Write the equivalent sum term for each binary number from Step 2 and express in POS form.

## Slide 21: Converting Standard SOP to Standard POS (example)

## Slide 22: Boolean Expressions & Truth Tables
All standard Boolean expression can be easily converted into truth table format using binary values for each term in the expression.
Also, standard SOP or POS expression can be determined from the truth table

## Slide 23: Converting SOP Expressions to Truth Table Format
Recall the fact:
An SOP expression is equal to 1 only if at least one of the product term is equal to 1.
Constructing a truth table:
Step 1: List all possible combinations of binary values of the variables in the expression.
Step 2: Convert the SOP expression to standard form if it is not already.
Step 3: Place a 1 in the output column (X) for each binary value that makes the standard SOP expression a 1 and place 0 for all the remaining binary values.

## Slide 24: Converting SOP Expressions to Truth Table Format (example)

## Slide 25: Converting POS Expressions to Truth Table Format
Recall the fact:
A POS expression is equal to 0 only if at least one of the product term is equal to 0.
Constructing a truth table:
Step 1: List all possible combinations of binary values of the variables in the expression.
Step 2: Convert the POS expression to standard form if it is not already.
Step 3: Place a 0 in the output column (X) for each binary value that makes the standard POS expression a 0 and place 1 for all the remaining binary values.

## Slide 26: Converting POS Expressions to Truth Table Format (example)
POS

## Slide 27: Determining Standard Expression from a Truth Table

## Slide 28: Determining Standard Expression from a Truth Table

## Slide 29: Determining Standard Expression from a Truth Table (example)

## Slide 30: SOP and POS forms SOP and POS
What is this: SOP or POS?
How would you make it into a SOP?
  “Multiply Out”  Distributive Law!!
How would you make it into a POS?
  “Factor”  Dual of Distributive Law!!

## Slide 31: Converting between SOP and POS
“Multiply out” to convert POS to SOP
  
“Factor” to convert SOP to POS
  
POS
SOP
x  (y + z) = x  y + x  z
x + y  z = (x + y)  (x + z)
Distributive Law
Distributive Law (Dual)
=
SOP
POS

## Slide 32: NAND and NOR Gates NAND Gate
Logical NAND
  Description:
    The output is the inverse (i.e. NOT) of an AND gate
  Symbolic Representation (NAND gate):
  Truth Table Representation:
  Boolean Description:
A | B | C
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
What happens if we “push” the bubble (from output to input)?

## Slide 33: NOR Gate
Logical NOR
  Description:
    The output is the inverse (i.e. NOT) of an OR gate
  Symbolic Representation (NOR gate):
  Truth Table Representation:
  Boolean Description:
A | B | C
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
What happens if we “push” the bubble (from output to input)?

## Slide 34: Exclusive OR operation -Exclusive-OR Gate
Exclusive-OR (XOR)
  Description:
    The output is true if one and only one of its inputs is true
  Symbolic Representation (XOR gate):
  Truth Table Representation:
  Boolean Description:
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A
B
C

## Slide 35: Exclusive OR operation Some Exclusive-OR Operations

## Slide 36: Exclusive OR operation-Exclusive-OR Gate
Exclusive-NOR (XNOR)
  Description:
    The output is true if all of its inputs are equivalent
  Symbolic Representation (XNOR gate):
  Truth Table Representation:
  Boolean Description:
A | B | C
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A
B
C
Sometimes referred to as the “equivalence” gate

## Slide 37: Converting SOP to NAND – NAND Circuits
An AND – OR circuit!!!
A NAND – NAND circuit!!!

Implementing SOP expressions using NAND gates:

## Slide 38: Converting POS to NOR – NOR Circuits
An OR – AND circuit!!!
An NOR – NOR circuit!!!

Implementing POS expressions using NOR gates:

## Slide 40: Review of Simplification Theorems
Uniting Theorem
Absorption Theorem
Elimination Theorem
Consensus Theorem
LHS=

## Slide 41: Proving Equations (Validity)
To prove the validity of an equation we can:
  Construct a truth table for each side of the eqn
    Need to observe all possible inputs and associated outputs
  Apply theorems to either or both sides
    Can apply duality to both the LHS and the RHS
    Can apply DeMorgan’s theorem (i.e. push bubbles)
  Could show that the circuit implementation of each side yields the same output- For possible ALL inputs

## Slide 42: Examples
Find the complement of
Convert the following into a SOP expression
Find the Dual of the Elimination Theorem
If, 

## Slide 43: Boolean Algebra -A Circuit Example
x + (y  z) = (x + y)  (x + z)
Distributive Law (Dual)
Determine the Output of the Following Circuit
Design a Simpler Circuit with the Same Output

## Slide 44: EXAMPLE
Ben is having a picnic. He won’t enjoy it if it rains or if there are ants. Design a circuit that will output TRUE only if Ben enjoys the picnic.
The inputs are A and R, which indicate if there are ants and if it rains.
A is TRUE when there are ants and FALSE when there are no ants.
Similarly for rain R
Using sum-of-products form, we write the equation as: E= A’R’

## Slide 45
The system has four inputs, A3, . . . , A0, and four outputs, Y3, . . . , Y0. These signals can also be written as A3:A0 and Y3:Y0.
Each user asserts her input when she requests the auditorium for the next day. The system asserts at most one output, granting the auditorium to the highest priority user. The dean, who is paying for the system, demands highest priority (3). The department chair, teaching assistant, and dorm social chair have decreasing priority.
Write a truth table and Boolean equations for the system. Sketch a circuit that performs this function.