## Slide 1
Introduction to
8086 and its Architecture

## Slide 2
Topics
First micro processor by Intel
8086 micro processor
Block diagram
and so on …

## Slide 3
PIN diagram of 8086

## Slide 4
Why 8086 is so special…. ? An million $ question
It introduced instruction cache / queue
That leads the modern processor with huge cache
That leads to MIPS architecture
and so on …

## Slide 5
Block diagram of 8086
EU – Execution unit
BIU – Bus interface unit
D(16)
A(20)
D(8)
Q(8)

## Slide 8
AX - the accumulator register (divided into AH / AL):
1. Generates shortest machine code
2. Arithmetic, logic and data transfer
3. One number must be in AL or AX
4. Multiplication & Division
5. Input & Output
BX - the base address register (divided into BH / BL).
CX - the count register (divided into CH / CL):
1. Iterative code segments using the LOOP instruction
2. Repetitive operations on strings with the REP command
3. Count (in CL) of bits to shift and rotate

## Slide 9
DX - the data register (divided into DH / DL):
1. DX:AX concatenated into 32-bit register for some MUL and DIV operations
2. Specifying ports in some IN and OUT operations
SI - source index register:
1. Can be used for pointer addressing of data
2. Used as source in some string processing instructions
3. Offset address relative to DS
DI - destination index register:
1. Can be used for pointer addressing of data
2. Used as destination in some string processing instructions
3. Offset address relative to ES

## Slide 10
BP - base pointer:
1. Primarily used to access parameters passed via the stack
2. Offset address relative to SS
SP - stack pointer:
1. Always points to top item on the stack
2. Offset address relative to SS
3. Always points to word (byte at even address)
4. An empty stack will had SP = FFFEh

## Slide 11
SEGMENT REGISTERS
CS - points at the segment containing the current program.
DS - generally points at segment where variables are defined.
ES - extra segment register, it's up to a coder to define its usage.
SS - points at the segment containing the stack
IP - the instruction pointer: Always points to next instruction to be executed
Offset address relative to CS
IP register always works together with CS segment register and it points to currently executing instruction.

## Slide 12
Association of Registers
CS - IP
DS – SI, BX
ES - DI
SS – BP, SP

## Slide 13
FLAG REGISTER

## Slide 14
Carry Flag (CF) - this flag is set to 1 when there is an unsigned overflow. For example when you add bytes 255 + 1 (result is not in range 0...255). When there is no overflow this flag is set to 0.
Parity Flag (PF) - this flag is set to 1 when there is even number of one bits in result, and to 0 when there is odd number of one bits.
Auxiliary Flag (AF) - set to 1 when there is an unsigned overflow for low nibble (4 bits).
Zero Flag (ZF) - set to 1 when result is zero. For non-zero result this flag is set to 0.
Sign Flag (SF) - set to 1 when result is negative. When result is positive it is set to 0. (This flag takes the value of the most significant bit.)
Trap Flag (TF) - Used for on-chip debugging.

## Slide 15
Interrupt enable Flag (IF) - when this flag is set to 1 CPU reacts to interrupts from external devices.
Direction Flag (DF) - this flag is used by some instructions to process data chains, when this flag is set to 0 - the processing is done forward, when this flag is set to 1 the processing is done backward.
Overflow Flag (OF) - set to 1 when there is a signed overflow. For example, when you add bytes 100 + 50 (result is not in range -128...127).

## Slide 16
Addressing Mode of 8086

## Slide 17
Types of Addressing mode
Register addressing mode
Immediate addressing mode
Direct addressing mode / displacement
Indirect addressing mode
Indexed addressing mode / index AM
Based Indexed addressing mode
Base indexed displacement addressing mode.

## Slide 18
Most 8086 instructions can operate on the 8086's general purpose register set. By specifying the name of the register as an operand to the instruction, you may access the contents of that register. Consider the 8086
mov destination, source

## Slide 19
Register addressing mode
mov ax, bx ;Copies the value from BX into AX
mov dl, al ;Copies the value from AL into DL
mov si, dx ;Copies the value from DX into SI
mov sp, bp ;Copies the value from BP into SP
mov dh, cl ;Copies the value from CL into DH
mov ax, ax ;Yes, this is legal!
Immediate addressing mode
mov ax, 10H ;
mov dl, FFH ;
mov si, ADH ;
mov sp, 123H;
mov dh, AH;

## Slide 20
Direct addressing mode
mov AL, DS:[8080h];
mov DS:[1234h], DL;
ES:[1000h];
CS:[ACh];

## Slide 21
Indirect addressing mode
mov al, [bx]
mov al, [bp]
mov al, [si]
mov al, [di]
mov al, cs:[bx]
mov al, ds:[bp]
mov al, ss:[si]
mov al, es:[di]

## Slide 22
Indexed addressing mode
mov al, disp[bx]
mov al, disp[bp]
mov al, disp[si]
mov al, disp[di]
mov al, ss:disp[bx]
mov al, es:disp[bp]
mov al, cs:disp[si]
mov al, ss:disp[di]
If bx contains 1000h, then the instruction mov cl, 20h[bx] will load cl from memory location ds:1020h.
Likewise, if bp contains 2020h, mov dh,1000h[bp] will load dh from location ss:3020.
You may substitute si or di in the figure above to obtain the [si+disp] and [di+disp] addressing modes.

## Slide 23
mov al, [bx][si]
mov al, [bx][di]
mov al, [bp][si]
mov al, [bp][di]
Based Indexed addressing mode
Suppose that bx contains 1000h and si contains 880h. Then the instruction
mov al,[bx][si]
would load al from location DS:1880h. Likewise, if bp contains 1598h and di contains 1004, mov ax,[bp+di] will load the 16 bits in ax from locations SS:259C and SS:259D.

## Slide 24
Base indexed displacement addressing mode
mov al, disp[bx][si]
mov al, disp[bx+di]
mov al, [bp+si+disp]
mov al, [bp][di][disp]
You may substitute di in the figure above to produce the [bx+di+disp] addressing mode.
You may substitute di in the figure above to produce the [bp+di+disp] addressing mode. Suppose bp contains 1000h, bx contains 2000h, si contains 120h, and di contains 5. Then mov al,10h[bx+si] loads al from address DS:2130; mov ch,125h[bp+di] loads ch from location SS:112A; and mov bx,cs:2[bx][di] loads bx from location CS:2007.

## Slide 25
Don’t worry 

## Slide 26
If you choose zero or one items from each of the columns and wind up with at least one item, you've got a valid 8086 memory addressing mode. Some examples:
Choose disp from column one, nothing from column two, [di] from column 3, you get disp[di].
Choose disp, [bx], and [di]. You get disp[bx][di].
Skip column one & two, choose [si]. You get [si]
Skip column one, choose [bx], then choose [di]. You get [bx][di]
disp[dx][si]

## Slide 27
Flag Register

## Slide 28
Carry Flag (CF) - this flag is set to 1 when there is an unsigned overflow. For example when you add bytes 255 + 1 (result is not in range 0...255). When there is no overflow this flag is set to 0.
Parity Flag (PF) - this flag is set to 1 when there is even number of one bits in result, and to 0 when there is odd number of one bits.
Auxiliary Flag (AF) - set to 1 when there is an unsigned overflow for low nibble (4 bits).
Zero Flag (ZF) - set to 1 when result is zero. For non-zero result this flag is set to 0.
Sign Flag (SF) - set to 1 when result is negative. When result is positive it is set to 0. (This flag takes the value of the most significant bit.)
Trap Flag (TF) - Used for on-chip debugging.

## Slide 29
Interrupt enable Flag (IF) - when this flag is set to 1 CPU reacts to interrupts from external devices.
Direction Flag (DF) - this flag is used by some instructions to process data chains, when this flag is set to 0 - the processing is done forward, when this flag is set to 1 the processing is done backward.
Overflow Flag (OF) - set to 1 when there is a signed overflow. For example, when you add bytes 100 + 50 (result is not in range -128...127).

## Slide 30
  |  | 
 64 K | ROM BIOS | F0000H - FFFFFH
  |  | 
384 K ROM | ROM BASIC | Present in older computers
 |  | 
 | Reserved ROM | 
 |  | 
 | Video BIOS ROM | C0000H - C7FFFH
 |  | 
 A0000H | Video RAM | A0000H - BFFFFH
 |  | 
 |  | 
 | User RAM | 
640 K RAM |  | 
 |  | 
 | Resident portion of DOS | Varies between 12 K to 40 K
 |  | 
 | BIOS and DOS data area | 00400H - 005FFH
 1 K | Interrupt Vector Table | 00000H - 003FFH
Memory Map of 8086 (for PC)
SimpleISR proc far mov ax, 0 iret SimpleISR endp