## Slide 1: NUMBER REPRESENTATION
20XC14 DIGITAL SYSTEM DESIGN

## Slide 2: NUMBER REPRESENTATION
Binary - Octal – Hexadecimal
BCD - excess three - Gray codes
Error correcting and detecting codes
Representation of signed numbers
Arithmetic operation on signed numbers
Alphanumeric data representation.

## Slide 3: Numbers
We use numbers
  to communicate
  to perform tasks
  to quantify
  to measure
Numbers have become symbols of the present era
Many consider what is not expressible in terms of numbers is not worth knowing

## Slide 4: Number Systems in use
Symbolic number system
  uses Roman numerals (I = 1, V = 5, X = 10, L = 50,C = 100, D = 500 and M = 1000)
still used in some systems
Weighted position system
Decimal system is the most commonly used
Decimal numbers are based on Indian numerals
Radix used is 10

## Slide 5: Other weighted position systems
Advent of electronic devices with two states created a possibility of working with binary numbers
Binary numbers are most extensively used
Binary system uses radix 2
Octal system uses radix 8
Hexa-decimal system uses radix 16

## Slide 6: Weighted Position Number System
Value associated with a digit is dependent on its position
The value of a number is weighted sum of its digits
2357 = 2 x 103 + 3 x 102 + 5 x 101 + 7 x 100
Decimal point allows negative and positive powers of 10
526.47 = 5 x 102 +2 x 101 + 6 x 100 + 4 x 10-1+ 7 x 10-2
10 is called the base or radix of the number system

## Slide 7: General positional number system
Any integer > 2 can serve as the radix
Digit position .i. has weight r i
The general form of a number is
p digits to the left of the point (radix point) and n digits to
the right of the point

## Slide 8: General positional number system (2)
The value of the number is
Leading and trailing zeros have no values
The values dis can take are limited by the radix value
A number like (357)5 is incorrect

## Slide 9: Binary Number System
Uses 2 as its radix
Has only two numerals, 0 and 1
Example:
(N)2 = (11100110)2
It is an eight digit binary number
The binary digits are also known as bits
(N)2 is an 8-bit number

## Slide 10: Binary numbers to Decimal Number
(N)2 = (11100110)2
Its decimal value is given by,

## Slide 11: Binary fractional number to Decimal number
A binary fractional number (N)2 = 101.101
Its decimal value is given by

## Slide 12: Number Systems and Conversion
53
2
26
2
13
2
6
2
3
2
1
2
rem. = 1 = a0
rem. = 0 = a1
rem. = 1 = a2
rem. = 0 = a3
rem. = 1 = a4
0
rem. = 1 = a5

## Slide 13: Number Systems and Conversion
  Convert Decimal 0.625 to base 2 (i.e., binary)

## Slide 14: Number Systems and Conversion( DECIMAL /BINARY)
Decimal:
(base 10)
Binary:
(base 2)
Base “R”

## Slide 15: Some features of Binary Numbers
Require very long strings of 1s and 0s
Some simplification can be done through grouping
3-bit groupings: Octal (radix 8) groups three binary digits
Digits will have one of the eight values 0, 1, 2, 3, 4, 5, 6,and 7
4-digit groupings: Hexa-decimal (radix 16)
Digits will have one of the sixteen values 0 through 15.
Decimal values from 10 to 15 are designated as A (=10),B (=11), C (=12), D (=13), E (=14) and F (=15)

## Slide 16: Number Systems and Conversion
Binary
000
001
010
011
100
101
110
111
QUESTION:
How many binary “bits” do we need to represent a single Octal digit?
Octal
0
1
2
3
4
5
6
7

## Slide 17: Number Systems and Conversion
Binary Hex Decimal
0000 0 0
0001 1 1
0010 2 2
0011 3 3
0100 4 4
0101 5 5
0110 6 6
0111 7 7
1000 8 8
1001 9 9
1010 A 10
1011 B 11
1100 C 12
1101 D 13
1110 E 14
1111 F 15
QUESTION:
How many binary “bits” do we need to represent a single Hexadecimal digit?

## Slide 18: Number Systems and Conversion
C
Converting to/from Binary, Hex, and Octal
  An example of converting Binary to Octal
  An example of converting Binary to Hexadecimal
5
1
1
2
7
1001101.0101112
= 115.278
D
4
5
1001101.0101112
= 4D.5C16

## Slide 19: EXAMPLES
  Base 8 to Decimal
  Base 16 to Decimal

## Slide 20: Changing the radix of numbers
Conversion requires, sometimes, arithmetic operations
The decimal equivalent value of a number in any radix
Examples

## Slide 21: Conversion of decimal numbers to numbers with radix r
Represent a number with radix r as
To convert a number with radix r to a decimal number
Divide the right hand side by r
Remainder: d0
Quotient:
Division of Q by r gives d1 as the remainder

## Slide 22: Example of Conversion
Quotient Remainder
678 ÷ 8 84 6
84 ÷ 8 10 4
10 ÷ 8 1 2
1 ÷ 8 0 1
(678)10 = (1246)8
Quotient Remainder
678 ÷ 16 42 6
42 ÷ 16 2 A
2 ÷ 16 0 2
(678)10 = (2A6)16

## Slide 23: Number Systems and Conversion
Example:
  Convert 231.34 to base 7
  First convert to decimal
  Convert the integer portion (4510 = ???7)
  Convert the decimal portion ( .7510 = .???7)
45
7
6
7
0
rem. = 6
rem. = 3
…

## Slide 24: EXERCISES
Decimal Binary Octal Hexadecimal
369.3125 ? ? ?
? 10111101.101 ? ?
? ? 326.5 ?
? ? ? F3C7.A
5. What is the decimal equivalent of the largest binary integer that can be obtained with (a) 11 bits and (b) 25 bits?

## Slide 25: EXERCISES
Perform the following conversion by using base 2 instead of base 10 as the intermediate base for the conversion:
(a) (673.6)8 to hexadecimal (b) (E7C.B)16 to octal (c) (310.2)4 to octal
2. Considerable evidence suggests that base 20 has historically been used for number systems in a number of cultures.
(a) Write the digits for a base 20 system, using an extension of the same digit representation scheme employed for hexadecimal.
(b) Convert (2007)10 to base 20.
(c) Convert (BCI.G)20 to decimal.
3. In each of the following cases, determine the radix r: (a) (BEE)r (2699)10 (b) (365)r (194)10

## Slide 26: Binary Arithmetic & Negative Numbers
Binary Arithmetic
  Addition and subtraction
  Multiplication and Division
Representation of Negative Numbers
  1’s complement, 2’s complement, and sign & magnitude

## Slide 27: Binary Arithmetic - ADDITION
Binary Addition
An Example of Binary Addition
0 + 0 = 0
0 + 1 = 1 + 0 = 1
1 + 1 = 0 and carry 1
1 1 0 1
+ 1 0 1 1
0
1
0
1
0
1
1
1
1
= 1310
= 1110
= 2410
 Carries

## Slide 28: Binary Arithmetic- SUBTRACTION
1 1 1 0 1
Binary Subtraction
An Example of Binary Subtraction
0 - 0 = 0
0 - 1 = 1 and borrow 1
1 - 1 = 0
1 - 0 = 1
1 1 1 0 1
 1 0 0 1 1
0
0 1
1
0
1
0
= 2910
= 1910
= 1010
 Borrows

## Slide 29: Binary Arithmetic- BINARY MULTIPLICATION
Binary Multiplication
An Example
0 X 0 = 0
0 X 1 = 1 X 0 = 0
1 X 1 = 1
1 1 0 1
= 1310
X 1 0 1 1
= 1110
1 1 0 1
1 1 0 1
0 0 0 0
1 1 0 1
1 0 0 1 1 1
1 1 0 1
+ 1 1 0 1
+ 0 0 0 0
1 0 0 1 1 1
+ 1 1 0 1
1 0 0 0 1 1 1 1
1 0 0 0 1 1 1 1
1st Partial sum
2nd Partial sum
Final prod
= 14310

## Slide 30: Binary Arithmetic -DIVISION
1 0 1 1
1 0 1 1 = 1310
1 0 0 1 0 0 0 1
1
1 0 1 1
0 1 1 1 0
1
1 0 1 1
0 0 1 1 0 1
0 1
1 0 1 1
1 0
 Remainder = 210
= 14510
= 1110

## Slide 31: Representation of Negative Numbers
 |  | … |  | 
Unsigned Number
Signed Number
Magnitude
MSB
LSB
 |  | … |  | 
Magnitude
MSB
LSB
Sign
Sign bit = 0  Positive Number
Sign bit = 1  Negative Number

## Slide 32: Representation of Negative Numbers
Three Representations of signed numbers
  Sign & Mag, 1’s Complement, and 2’s Complement
All represent positive numbers in the same way
How to generate a negative number:
  Sign & Mag
    Simply change the sign bit
  1’s Complement
    Simply flip all of the bits
  2’s Complement
    Simply flip all of the bits and add 1
Easy for us to read
Simple to generate a negative Number
Easy for computer arithmetic

## Slide 33: Representation of Negative Numbers
Three Representations
  Sign & Mag, 1’s Complement, and 2’s Complement
+N | All three the Same
+0 | 0000
+1 | 0001
+2 | 0010
+3 | 0011
+4 | 0100
+5 | 0101
+6 | 0110
+7 | 0111
-N | Sign & Magnitude
-0 | 1000
-1 | 1001
-2 | 1010
-3 | 1011
-4 | 1100
-5 | 1101
-6 | 1110
-7 | 1111
Positive Integers
Negative Integers
1’s Complement
1111
1110
1101
1100
1011
1010
1001
1000
2’s Complement
-
1111
1110
1101
1100
1011
1010
1001
-8 - - 1000

## Slide 34: Representation of Negative Numbers
Addition and Subtraction
  Sign and Magnitude
    Simple if both numbers have the same sign
    More complex if the signs differ
    Two different representations of “0” is problematic
  1’s Complement
    Addition and subtraction not so simple
    Two different representations of “0” is problematic
  2’s Complement
    Both addition and subtraction are simple

## Slide 35: 2’S Complement Process
The steps in the 2’s Complement process are similar to the 10’s Complement process. However, you will use the base two.
First, complement all of the digits in a number.
  A digit’s complement is the number you add to the digit to make it equal to the largest digit in the base (i.e., 1 for binary). In binary language, the complement of 0 is 1, and the complement of 1 is 0.
Second, add 1.
  Without this step, our number system would have two zeroes (+0 & -0), which no number system has.
Notes: This slide describes the 2’s complement conversion process.

## Slide 36: Two’s Complement
Positive numbers remain the same
Negative numbers: derived by flipping each bit and then adding 1 to the result
  +19 in 6 bits = 010011,
  -19 in 6 bits = 101101
    010011  101100 +1  101101
  To convert back, flip all bits except sign bit and add 1
    1 01101  1 10010 + 1  1 10011
  While this is harder, it has two advantages
    Only 1 way to represent 0 (000000) so we can store 1 extra value that we lost when we tried signed magnitude and one’s complement
    Arithmetic operations do not require “peeling” off the sign bit
Notes: Two’s complement is harder but worthwhile since we can store 256 different values in 8 bits.
Aside from the conversion technique shown above, a shortcut method is to convert the number right-to-left by copying each bit exactly as it is through the first 1 bit, and then flip all remaining bits after the first 1.
11110100  starting right to left, copy down all bits through the first 1 giving us …100, now flip all remaining bits (11110 becomes 00001) giving us 00001100.
Let’s check to make sure this was done properly by using the other approach: 11110100  flip all bits giving 00001011 and add 1, 00001011 + 1 = 00001100, so it worked!
Convert 01011010  copy all bits through the first 1  …10, now flip all remaining bits (010110 becomes 101001)  10100110.
Confirm this by trying the other way: 01011010  10100101 + 1 = 10100110

## Slide 38: 2’s Complement Examples
Example #1
Example #2
Complement Digits
Add 1
5 = 00000101
-5 = 11111011

11111010
+1
Complement Digits
Add 1
-13 = 11110011
13 = 00001101

00001100
+1
Notes: Examples of the 2’s Complement Process.

## Slide 39: Examples
Represent 83 and –83 using 8 bits in all 3 signed representations:
+83 = 64 + 16 + 2 + 1 = 01010011 (in all 3 representations)
-83:
Signed magnitude = 11010011 (sign bit is 1 for negative)
One’s complement = 10101100 (flip all bits from +83)
Two’s complement = 10101101 (flip all bits from +83 and add 1)
Convert 11110010 into a decimal integer in all 4 representations
Unsigned magnitude = 128 + 64 + 32 + 16 + 2 = 242
Signed magnitude = -114 (negative, 1110010 = 114)
One’s complement = -13 (leading bit = 1, the number is negative,flip all bits 10001101 = 13)
Two’s complement = -14 (negative, so flip all bits and add 1 
10001101 + 1 = 10001110 = 14)
Notes: See the web site for more examples.

## Slide 40: The Number Circle
Clockwise: increment
Anti-clockwise: decrement
0000 (0)
0001 (1)
0010 (2)
0100 (4)
0011 (3)
0111 (7)
1000 (8)
0101 (5)
0110 (6)
1100 (12)
1011 (11)
1101 (13)
1001 (9)
1010 (10)
1110 (14)
1111 (15)
Increment
40

## Slide 41: Number Circle with Negative Numbers
break point
0000 (0)
0001 (1)
0010 (2)
0100 (4)
0011 (3)
0111 (7)
1000 (-8)
0101 (5)
0110 (6)
1100 (-4)
1011 (-5)
1101 (-3)
1001 (-7)
1010 (-6)
1110 (-2)
1111 (-1)
Increment
41
Clockwise: increment
Anti-clockwise: decrement

## Slide 42
Graphical Representation of 2’s Complement Numbers
  Largest positive number is +(2n-1 -1)
  Largest negative number is -(2n-1)

## Slide 43: Using the Number Circle
To add M to a number, N
  locate N on the number circle
  If M is +ve
    Move M steps clockwise
  If M is -ve
    Move M steps anti-clockwise, or 2n – M steps clockwise
  If we cross the break-point
    We have an overflow
    The number is too large/ too small to be represented
43

## Slide 44: Binary Arithmetic
2’s Complement Addition
  In 2’s complement addition ignore carry-out from MSB
  Overflow occurs if:
    Sum of two positive numbers is negative, or
    Sum of two negative numbers is positive
0 1 0 1
+5
0 0 1 0
+2
0 1 1 1
+7
1 0 1 1
-5
0 0 1 0
+2
1 1 0 1
-3
1 0 1 1
-5
1 1 1 0
-2
1 1 0 0 1
-7
Ignore Carry out from MSB
0 1 0 1
+5
0 1 1 0
+6
1 0 1 1
+11
Overflow Occurred
1 0 1 1
-5
1 0 1 0
-6
1 0 1 0 1
-11
Overflow Occurred
Result does NOT
fit in the number
of bits available

## Slide 45: Using The 2’s Complement Process
9
+ (-5)
4
(-9)
+ 5
- 4
(-9)
+ (-5)
- 14
9
+ 5
14
POS
+ POS
POS

POS
+ NEG
POS

NEG
+ POS
NEG

NEG
+ NEG
NEG

Use the 2’s complement process to add together the following numbers.
Notes: This slide show that there are only four possible combinations for adding together two signed numbers. The next four slides demonstrate each of these examples.

## Slide 46: POS + POS → POS Answer
If no 2’s complement is needed, use regular binary addition.
00001001
9
+ 5
14


00001110
00000101

+
Notes: Addition of two Positive numbers.

## Slide 47: POS + NEG → POS Answer
Take the 2’s complement of the negative number and use regular binary addition.
00001001
9
+ (-5)
4


11111011
+
00000101

11111010
+1
11111011
2’s
Complement
Process
1]00000100
8th Bit = 0: Answer is Positive
Disregard 9th Bit
Notes: This example shows the addition of one positive and one negative numbers. Note that this is done in the same way as subtracting a positive number from a positive number. In this case, the answer is positive.

## Slide 48: POS + NEG → NEG Answer
Take the 2’s complement of the negative number and use regular binary addition.
11110111
(-9)
+ 5
-4


00000101
+
00001001

11110110
+1
11110111
2’s
Complement
Process
11111100
8th Bit = 1: Answer is Negative
11111100

00000011
+1
00000100
To Check:
Perform 2’s
Complement
On Answer
Notes: This slide demonstrates the addition of one positive and one negative number. Again, this is is the same a subtracting a positive number from a positive number. In this case the answer happens to be negative.

## Slide 49: NEG + NEG → NEG Answer
Take the 2’s complement of both negative numbers and use regular binary addition.
11110111
(-9)
+ (-5)
-14


11111011

+
2’s Complement
Numbers, See
Conversion Process
In Previous Slides
1]11110010
8th Bit = 1: Answer is Negative
Disregard 9th Bit
11110010

00001101
+1
00001110
To Check:
Perform 2’s
Complement
On Answer
Notes: This slide demonstrates the addition of two negative numbers.

## Slide 50: Subtraction
F(u-v) ≡ F(u) + F(-v)
≡ F(u) + 2n - F(v)
Subtraction is the same as addition
Compute the 2's complement of F(v)
50
11010100  11010100
- 00110011 + 11001101
110100001
Notice the overflow in this case too, but it differs from the last example because we are using two’s complement

## Slide 51: POS - POS → POS +NEG
If no 2’s complement is needed, use regular binary addition.
00001001
9
+(-5)
4


100000100
11111011

+
9
- 5
4
8th Bit = 0: Answer is Positive
Disregard 9th Bit
Notes: Addition of two Positive numbers.

## Slide 52: POS - NEG → POS +POS
Take the 2’s complement of the negative number and use regular binary addition.
00001001
9
- (-5)
14


00000101
+
11111011
2’s
Complement
Process
0]00001110
8th Bit = 0: Answer is Positive
Disregard 9th Bit
9
+(+5)
14
00000100
00000101
+1
Notes: This example shows the addition of one positive and one negative numbers. Note that this is done in the same way as subtracting a positive number from a positive number. In this case, the answer is positive.

## Slide 53: NEG- NEG → NEG +POS
Take the 2’s complement of the negative number and use regular binary addition.
11110111
(-9)
+ 5
-4


00000101
+
00001001

11110110
+1
11110111
2’s
Complement
Process
11111100
8th Bit = 1: Answer is Negative
11111100

00000011
+1
00000100
To Check:
Perform 2’s
Complement
On Answer
(-9)
- (-5)
-4
Notes: This slide demonstrates the addition of one positive and one negative number. Again, this is is the same a subtracting a positive number from a positive number. In this case the answer happens to be negative.

## Slide 54: NEG – POS= NEG+NEG
Take the 2’s complement of both negative numbers and use regular binary addition.
11110111
(-9)
+ (-5)
-14


11111011

+
2’s Complement
Numbers, See
Conversion Process
In Previous Slides
1]11110010
8th Bit = 1: Answer is Negative
Disregard 9th Bit
11110010

00001101
+1
00001110
To Check:
Perform 2’s
Complement
On Answer
(-9)
-(+5)
-14
Notes: This slide demonstrates the addition of two negative numbers.

## Slide 56: Overflow
When adding 2 n-bit numbers it is possible to get a n+1 bit result if there is a carry out.
In 2’s complement add a MSB 0 for a positive or a MSB 1 for a negative.
In a computer the number of bits that can be used is fixed.

## Slide 57: Overflow indication.
In 8-bit 2’s complement notation the range that can be represented is -127 to +127.
Then the operation to add +70 to +80 is
  Carries 0 1
  +70 0 100 0110
  +80 0 101 0000
  +150 1 001 0110
Also look at the addition of -70 and -80

## Slide 58: The other addition
The addition of -70 and -80
  Carries 1 0
  -70 1 011 1010
  -80 1 011 0000
  -150 0 110 1010
The rule – if the carry into the MSB position differs from the carry out from the MSB position then an overflow has occurred.
.

## Slide 59: Overflow Rules
In unsigned magnitude addition
  a carry out of the left-most bit is also an overflow
In unsigned magnitude subtraction
  overflow will occur in subtraction if we must borrow prior to the left-most bit
In two’s complement addition/subtraction
  if the two numbers have the same sign bit and the sum/difference has a different sign bit, then overflow
Below we see examples of four signed additions

## Slide 60: Representation of Negative Numbers
2’s Complement Subtraction
  Just don’t do it!!
  To subtract B from A add A and (-B)
  A – B = A + (-B)
Overflow is NOT carry !!
Carry is NOT overflow !!